## Slide 1: Computer Vision-based Path Planning for Robot Manipulator Using Bézier Curves
CHEUNG Dick Ho (WKT06a-24)
Supervisor: Professor Tim Woo
Bézier Curve
Computer Vision
Notes: Good morning everyone, my name is Dicaprio and this is my FYP. Before I begin, I would like to re-title my FYP into Bezier Curve based Path Planning, for Robot Manipulator, Using Computer Vision. I realized that my original title is a bit confusing after the midterm poster presentation day, but it is a bit too late to change the title in Febuary.

## Slide 2: TABLE OF CONTENTS 01 02 03 04
Project Objective
Methodology
Performance Evaluation
Video Demo
Notes: (Skip)

## Slide 3: PROJECT OBJECTIVE 01
Why I did this project?
Notes: (Skip)

## Slide 4: Main Objective
Computer Vision
Bézier Curve
Robotic Arm
Chinese Calligraphy Robot
Combine:
As no one has combined all 3 elements before
Notes: So, the main objective of my FYP is to combine Computer Vision Machine Learning Model, Bezier Curve Path Plannnig, and Robotic Arm into a real life application of a Chinese Calligraphy Robot. As no one has combined all 3 elements together before.

## Slide 5
WHY CHINESE CALLIGRAPHY?
Notes: You might ask, Why Chinese Calligraphy?

## Slide 6: Because Chinese Calligraphy Visualizes 3D Trajectory
Lift up = Thin strokes
Press Down = Thick strokes
Why 3D? Thickness of brush strokes = Height
Notes: I chose Chinese calligraphy as my application because Chinese calligraphy can visualize 3D Trajectory clearly. You might ask, Why is it 3D when the paper is 2D? It is because if we draw a line with the Chinese Calligraphy brush high in the air, the stroke drawn would be thin. If we press the brush onto the paper, the stroke would be thick. So, the thickness of the resulting brush strokes it draws can show the height of the trajectory, hence visualizing all 3 dimensions of the path planning algorithm.

## Slide 7: METHODOLOGY 02
How I did this project?
Notes: Now, let’s talk about how my project works.

## Slide 8: Experiment Setup
Notes: So, this is the setup of my FYP. There is the robotic arm on the left that writes Chinese calligraphy on the white paper, the camera in the center for the computer vision system, and my laptop on the right with a UI that controls the whole system.

## Slide 9: Workflow
CNN Model
Calibrate Writing Height
Computer Vision System
Fetch 2D Control Points
Generate 3D
Control Points
Control Point Generation
3D Bézier Splines
Add Connecting
Hermite Curves
Trajectory Generation
Control Robotic Arm
Chinese Calligraphy
Robot Manipulation
Notes: This is the workflow of my system and I will talk about it in detail.

## Slide 10: Computer Vision System
CNN Model
Calibrate Writing Height
Computer Vision System
Fetch 2D Control Points
Generate 3D
Control Points
Control Point Generation
3D Bézier Splines
Add Connecting
Hermite Curves
Trajectory Generation
Control Robotic Arm
Chinese Calligraphy
Robot Manipulation
Notes: The first part is the computer vision system.

## Slide 11
As Brush Height affects Stroke Thickness,
Notes: As I mentioned before, the height of the brush is important as it affects the stroke thickness

## Slide 12: and the Brush is NOT fixed on the Gripper
So, we need to calibrate where the gripper is holding the brush.
i.e. calibrate the distance between the gripper and the paper
when the brush touches the paper.
Notes: And I did not fix the brush onto the robotic arm like other similar projects. So, I need to calibrate where the gripper is holding the brush by detecting when/where the brush touches the paper.

## Slide 13: So, I use a Camera to detect if the brush touches the paper or not
Notes: So, I added this camera in the middle to see whether the brush touches the paper or not.

## Slide 14: Computer Vision Dataset
maobi_on_paper | maobi_off_paper | no_maobi
The Brush is Bent | The Brush is Straight | There is No Brush
268 Images | 463 Images | 63 Images + 200 Random Images
Annotated 994 Images, Augmented to 2386 Images
Notes: And these are the images taken with that camera. I splited it into 3 classes: maobi_on_paper where the brush is touching the paper and is bent; maobi_off_paper where the brush is Not touching the paper and is straight; and no_maobi where the brush is outside the view of the camera. I annotated 994 images and augmented these 994 images into 2386 Images for my dataset.

## Slide 15: CNN Object Classification Model
700 Epoches, Best Validation Accuracy: 94.472%
Notes: I trained my CNN Object Classification model on this dataset for 700 epochs and the best validation accuracy is 94.4%.

## Slide 16: Gripper Writing Height Calibration
Notes: This is the result of the model. I lower the brush until it shows maobi_on_paper. Then, lift it up until it is maobi_off_paper. The height of the robotic arm’s gripper would be my calibrated value.

## Slide 17: Control Point Generation
CNN Model
Calibrate Writing Height
Computer Vision System
Fetch 2D Control Points
Generate 3D
Control Points
Control Point Generation
3D Bézier Splines
Add Connecting
Hermite Curves
Trajectory Generation
Control Robotic Arm
Chinese Calligraphy
Robot Manipulation
Notes: So, the next part is the control point generation.

## Slide 18: Fetch 2D Control Points
From Make Me a Hanzi Dataset
Notes: I fetch the 2D control points of the chosen Chinese characters from an open-source dataset called Make Me a Hanzi. It includes the red control points and the white boundary in stroke order.

## Slide 19: Calculate 3D control points
using Largest Fitting Circles
Notes: So, I developed a largest fitting circles algorithm to convert the 2D control points to 3D. From each red control points, I increases the radius of the circle until it touches the boundary of the stroke. The size of these circles represent the stroke thickness, thus we can calculate their corresponding height of the Chinese calligraphy brush, which is the Z coordinates. So, we have 3D control points.

## Slide 20: Trajectory Generation
CNN Model
Calibrate Writing Height
Computer Vision System
Fetch 2D Control Points
Generate 3D
Control Points
Control Point Generation
3D Bézier Splines
Add Connecting
Hermite Curves
Trajectory Generation
Control Robotic Arm
Chinese Calligraphy
Robot Manipulation
Notes: After we have the control points, we connect them into trajectories.

## Slide 21: CONCEPTS
Hermite Curve
I connect 2 control points together with Hermite curve.
But we are missing v0 and v1
Catmull-Rom Spline
So, I uses Catmull-Rom Spline to calculate v0 and v1 to connect multiple Hermite curves
Notes: I uses Hermite curve, which is a variant of Bezier curve, to connect 2 control points together. As there are more than 2 control points in a stroke, I tried to use Catmull-Rom Spline to calculate the control velocities v0 and v1 of the Hermite curve to connect multiple Hermite curves together.

## Slide 22: But Catmull-Rom Spline is not good
Notes: However, Catmull-Rom Spline creates these strange backward movement as the control points are not uniformly spaced.

## Slide 23: Modified Catmull-Rom Spline
Notes: So, I modified the Catmull-Rom spline by limiting the magnitude of the control velocities to the distance to the closest control points. This prevents those backward movement and this is the result.

## Slide 24: Connecting Hermite Curves
First version for 2D Spline Algorithm
Final version for 3D Spline Algorithm
Notes: After connecting the control points within a stroke, I added these red connecting Hermite curves to control it to lift up the brush and go to the next stroke. Originally, I uses this Hermite curve that directly goes up and down to connect them. However, the sudden change of direction from going horizontally along the paper to vertically up is not smooth. Therefore, I modified the starting velocity vector into this horizontal along the previous movement direction to make it smoothly lift up the brush with G1 continuity.

## Slide 25: Brush Correction Algorithm*
*Not included in Final Report
ERROR!
Notes: After some testing, I found that the reason why it can’t write complex strokes clearly is because there is an error distance between the brush body and the brush tip. This cause it to move diagonally when it needs to move in a L shape. I thought of a way to correct this error AFTER I submitted my final report so this is not included in the report.

## Slide 26: Brush Correction Algorithm*
*Not included in Final Report
Notes: So, I shift the original control points in the direction from previous point to current point. So, if it is a straight line, the shifted position is still on the line. But if the line is in L-shaped, it would go a little bit outward to compensate the error.

## Slide 27: Robot Manipulation
CNN Model
Calibrate Writing Height
Computer Vision System
Fetch 2D Control Points
Generate 3D
Control Points
Control Point Generation
3D Bézier Splines
Add Connecting
Hermite Curves
Trajectory Generation
Control Robotic Arm
Chinese Calligraphy
Robot Manipulation
Notes: Finally, it’s robot manipulation part.

## Slide 28: User Interface
Notes: I created a simple UI to control the movement of the robotic arm. Users can choose which fai chun they want to write. They can also input their own custom characters.

## Slide 29: New LLM Feature*
Q: 幫我寫一個
關於春節的四字詞語。
(Help me write a
four-character idiom
related to the
Spring Festival.)
A: 大吉大利
(Great luck
and great profit)
ChatGPT - 4o
*Not included in Final Report
Notes: After I submitted the Final Report, I added a new LLM Feature by calling the API of HKUST ChatGPT-4o. Users can input a topic or a festival into the prompt and ChatGPT can help you think and input some relevant Fai Chun for the robotic arm to write.

## Slide 30: PERFORMANCE EVALUATION 03
How well it works
Notes: My last objective statement is to evaluate the performance boost of this Bezier curve path planning when compare to traditional methods.

## Slide 31: Developed 3 Path Planning Algorithms to compare & evaluate the result
Straight Line
BENCHMARK ALGORITHM
2D Bézier Spline
INTERMEDIATE ALGORITHM
3D Bézier Spline
FINAL ALGORITHM
Notes: So, I developed 3 different algorithms to compare their performace, which are the straight line benchmark algorithm that connects everything with straight line, the 2D Bezier Spline Algorithm which is a algorithm before I think of the largest fitting circle and the final 3D Bezier spline algorithm.

## Slide 32: Straight Line Benchmark Algorithm
Notes: The Straight line algorithm directly uses the fetched control points and connect them with straight line. This can act as a benchmark to evaluate other algorithms.

## Slide 33: 2D Bézier Spline Intermediate Algorithm
Notes: 2D Bezier Spline algorithm add a fixed height for the control points. So, the result has relatively uniform thickness.

## Slide 34: 3D Bézier Spline Final Algorithm
Notes: The final 3D Spline Algorithm has varying height, which creates varying brush thickness in the written words.

## Slide 35: 44.53% 41.66%
Faster for 2D Spline than Straight Line
Faster for 3D Spline than Straight Line
Comparison Data
Notes: I tested all 3 algorithms on many different characters and Fai Chuns and I recorded their time. The 2D Spline Algorithm is 44.53% faster than Straight Line Benchmark and 3D Spline is 41.66% faster

## Slide 36: VIDEO DEMO 04
How well it works
Notes: My last objective statement is to evaluate the performance boost of this Bezier curve path planning when compare to traditional methods.

## Slide 37: Demo in FYP Industry Day
Notes: Here is a Demo in FYP Industry Day.

## Slide 38: THANKS
Computer Vision-based Path Planning for Robot Manipulator Using Bézier Curves
CHEUNG Dick Ho (WKT06a-24)
Supervisor: Professor Tim Woo
Notes: And this is a timelapse of my FYP Industry day.

## Slide 39: Questions & Answers